## Slide 1: GDP Group 18
Unmanned Aircraft Camera Module
Notes: Michael Start
Welcome

## Slide 2: The Next 20 Minutes
Recap
Specification and Progress Overview
Implementation
Testing
Demo
Evaluation
Future Work
Conclusion
Questions
Notes: Michael
Describe our project: problem, specification, etc
How we’ve managed the project so far
Progress
Future plans

## Slide 3: Recap
Notes: Michael

## Slide 4: Problem
Currently, an autopiloted UAV may take pictures while it is in the air
On many UAV systems the aircraft must land before images can be downloaded and viewed
These images could be inadequate
Wireless transmission of images preferred
Notes: Michael

## Slide 5: SkyCircuits Autopilot (SC2)
http://www.skycircuits.com/
Notes: Michael

## Slide 6: Specification & Progress Overview
Notes: John

## Slide 7: Block Diagram
Notes: John“To design, build and test an electronic module capable of capturing still images from an unmanned aerial vehicle (UAV) and transmitting the images to a base station. The module must use the UAV autopilot’s low-bandwidth RS485 serial link (38.4 kBaud). A program must be written to interface with the base station software over a TCP/IP link, allowing image data to be received and displayed to the user. The electronic module will be constructed using strip-boards and will later be implemented on PCB if time is available.

## Slide 8: Spec: High Priority
Prompt (from base station) to capture and download image
Progressive Image encoding/decoding
Minimise download time (less than 3 minutes)
Notes: John

## Slide 9: Spec: High Priority
Prompt (from base station) to capture and download image
  GUI functional
Progressive Image encoding/decoding
  Lowered in priority, some code written
Minimise download time (less than 3 minutes)
  Approximately 8s capture + 12s download for 640x480
Notes: John

## Slide 10: Spec: Medium Priority
Module weight < 250g
Image resolution: 640 x 480
Cancel image download whilst downloading
Notes: John

## Slide 11: Spec: Medium Priority
Module weight < 250g
  ~70g
Image resolution: 640 x 480
Cancel image download whilst downloading
Notes: John

## Slide 12: Spec: Low Priority
Resend an image if corrupted
Interrupt download of image, save incomplete image
Select resolution of image
Display progress indicator of download
(User defined) Automatic image capture
Colour images
Select between colour / BW
Notes: John

## Slide 13: Spec: Low Priority
Resend an image if corrupted
  Automatic Repeat reQuests (ARQ)
Interrupt download of image, save incomplete image
Select resolution of image
Display progress indicator of download
Notes: John

## Slide 14: Spec: Low Priority (cont.)
(User defined) Automatic image capture
  Autopilot script triggers on waypoints, height, etc.
Colour images
Select between colour / BW

## Slide 15: Spec: Deliverables
Hardware: Constructed camera module
Software: Firmware for module, Software for base station
Documentation: Technical and User Documentation
Public Repository: Open source, publically accessible repository, includes all the above
Notes: John

## Slide 16: Spec: Deliverables
Hardware: Constructed camera module
  All on PCB
Software: Firmware for module, Software for base station
Documentation: Technical and User Documentation
Public Repository: Open source, publically accessible repository, includes all the above.
  https://github.com/uavcamera/uavcamera
Notes: John

## Slide 17: Implementation

## Slide 18: Ground Station -> Payload Communication
Autopilot -> Payload comms: Message sending
Autopilot
Payload
Message
Ground Station
Console Port
Our GUI

## Slide 19: Ground Station <- Payload Communication
Payload -> Autopilot comms: Shared memory
Autopilot
Payload
Shared memory
Ground Station
Data Port
Our GUI

## Slide 20: Commands
10 Commands
Uses Automatic Repeat reQuest (ARQ)
  For image data acknowledgment sent every 50 data packets
E.g. Image Download Request:
  0x02 0xXX 0xXX
Command ID
Image ID to Download (LSB)
Image ID to Download (MSB)

## Slide 21: Camera Communication
JPEG images at:
  80 x 64
  168 x 128
  320 x 240
  640 x 480
SD card used as storage
Autopilot

## Slide 22: Physical Implementation

## Slide 23: Tools Used
C# .NET for GUI (Visual Studio 2010)
C++ (including Sanguino libraries) Eclipse
MATLAB for progressive image testing
gEDA for schematics/PCB layouts
Git for version control

## Slide 24: Cost to Reproduce
 | Through Hole | Surface Mount
PCB (15 day, PCBtrain, ex. Delivery) | £33.08 | £33.08
Components (Farnell, inc. VAT, delivery) | £22.63 | £25.84
Camera (inc. VAT, ex. Delivery) | £52.80 | £52.80
TOTAL | £108.51 | £111.72

## Slide 25: Testing

## Slide 26: Debugging
Implemented simple debug interface for payload over SPI
Testing central to debugging implementation

## Slide 27: Test Plan
Iterative testing during implementation
Design
Prototype
Test

## Slide 28: Camera Testing
Establishing Contact
Getting Image

## Slide 29: Payload to Autopilot Communications Testing
Basic Connection
(Tx Tokens)
Setting Shared memory
and Sending Messages
Image Sending
Over Autopilot Link
Reliable Transmission using ARQs

## Slide 30: Ground Station Software Testing
Streaming Data from
SkyCircuits Software
Sending Command to
SkyCircuits Console Port
Image Capture and Download Using GUI
Basic Image Download via Autopilot Link

## Slide 31: ARQ Testing
Packet loss simulated
  1 in 100 probability of packet dropping.
  Software resent commands and image data that were not acknowledged.

## Slide 32: JPEG Header Extractor Testing
DCT and Huffman tables extracted
Extraction results compared with open source model (JPEGsnoop)
Tested against a variety of 640x480 images

## Slide 33: Final Testing

## Slide 34: Final Testing
Speed (at 640x480) – No Dropped Packets:
  ~8s Capture
  ~12s Download
  ~20s Total
Weight:
  ~53g Without camera case
  ~70g With camera case

## Slide 35: Demo

## Slide 36: Evaluation

## Slide 37: Streams
Acquired working camera
Got image off camera
Payload communicating with camera
Our software communicating with Autopilot via GS software
Payload communicating with autopilot
Working GUI
PCB Implementation
Autopilot debugging

## Slide 38: Management
Regular group meetings and progress reviews
  Helped identify problems early
  Minutes for when we needed to refer back to them
Good Communication
  Email, telephone, IRC, meetings, source control

## Slide 39: Obstacles
Two camera failures
  Ordered new cameras, modified project plan to fit around first delay, postponed flight test due to second.
Bug in Autopilot code
  Extensive debugging alongside supplier of autopilot.

## Slide 40: Future Work
Progressive Image Transfer
Multiple cameras at once (possibly 3D)
Multiple types of camera
Video Streaming
SD file system access
HDR Photography
Image processing (e.g. for target fixation)

## Slide 41: Conclusion

## Slide 42: Conclusion
As previously mentioned, most of specification was completed on time, under budget.
Elements that weren’t completed, there’s a good reason for. Mostly low-priority tasks.
We have delivered a working system to our customer. ##FINGERS CROSSED FOR TOMORROW##

## Slide 43: Questions?